## Slide 1: Hello,

## Slide 2
Verification of Hardware Accelerator for Cryptographic Applications
Under the guidance of Mr. Shridhar Nayak
By ,
Bhuvana Chandra Deepak M - 201038003
Shree Jnanesh - 201038012
Abhishek M H - 201038026

## Slide 3: Contents
Specification of Design Units
Verification Plan
Verification Environment
Testcases for Encryption
Testcases for Decryption
Testcases for Memory
Results
References

## Slide 4: Specification of Design Units
1GHz operating frequency (clk)
115 pipelines stages
64-bitlength input data
64-bitlength Output data Encryption & decryption
64-bitlength Key
512 Bytes Memory
Encryption DUT
  Clk – 1 bit
  Msg – 64 bit
  Key – 64 bit
  Cipher – 64 bit
Decryption DUT
  Clk – 1 bit
  Cipher – 64 bit
  Key – 64 bit
  Msg – 64 bit
Pin Details
4
Memory DUT
  Clk – 1bit
  Read/Write Enable – 1bit
  Data IO line – 64bit
  Key IO line – 64bit
  Address Input line – 6bit

## Slide 5: Verification Plan
Project schedule
Verification approach
Test definitions
Testbench requirements
Results Checking
Issue tracking

## Slide 6: Verification System Verilog Environment

## Slide 7: Verification UVM Environment

## Slide 8: Testcases for Encryption
Test Case Number | Test Case | Signal | Signal Value | Expected Output | Expected Result
1 | Negative clock edge | clk | LOW | Cipher is not changed, previous output are held as it is | PASS
 | Positive clock edge |  | HIGH | Cipher should vary according to DES Algorithm | PASS
2 | key given is 64 bit wide | key | 64 bit | Cipher will be as expected according to DES Algorithm | PASS
 | key length is less than 64 bit |  | <64 bit | An unknown value comes across the Cipher terminals | FAIL
 | key length is more than 64 bit |  | >64 bit | The first 64 bits are considered from key and Cipher is as per DES Logic | FAIL
3 | Message input is 64 bit wide | msg | 64 bit | Cipher will be as expected according to DES Algorithm | PASS
 | Message is less than 64 bit wide |  | <64 bit | An unknown value comes across the Cipher terminals | FAIL
 | Message is more than 64 bit wide |  | >64 bit | The first 64 bits are considered from msg and Cipher is as per DES Logic | FAIL
4 | When keys are changed for the same message | Msg,key | 64 bit | Different Cipher texts should be obtained. | PASS
5 | When Same Key is used with different messages | Msg,key | 64 bit | Cipher will occur as per DES Logic in different cycles | PASS

## Slide 9: Testcases for Decryption
Test Case Number | Test Case | Signal | Signal Value | Expected Output | Expected Result
1 | Negative clock edge | clk | LOW | Decrypt is not changed, previous output are held as it is | PASS
 | Positive clock edge |  | HIGH | Decrypt should vary according to DES Algorithm | PASS
2 | key given is 64 bit wide | key | 64 bit | Decrypt will be as expected according to DES Algorithm | PASS
 | key length is less than 64 bit |  | <64 bit | An unknown value comes across the Decrypt terminals | FAIL
 | key length is more than 64 bit |  | >64 bit | The first 64 bits are considered from key and Decrypt is as per DES Logic | FAIL
3 | cipher input is 64 bit wide | cipher | 64 bit | Decrypt will be as expected according to DES Algorithm | PASS
 | cipher is less than 64 bit wide |  | <64 bit | An unknown value comes across the Decrypt terminals | FAIL
 | cipher is more than 64 bit wide |  | >64 bit | The first 64 bits are considered from cipher and Decrypt is as per DES Logic | FAIL
4 | When keys are changed for the same message | cipher,key | 64 bit | Original message should not be obtained at Decrypt for different Key | PASS
5 | When Same Key is used with different messages | cipher,key | 64 bit | Decrypt will occur as per DES Logic in different cycles | PASS

## Slide 10: Testcases for Memory Block
Test Case Number | Test Case | Signal | Signal Value | Expected Output | Expected Result
1 | Negative clock edge | clk | LOW | Output lines should not change values even if Input given is changed. | PASS
 | Positive clock edge |  | HIGH | Output lines should read data from memory as per the Read Enable input whereas Input lines should write data as per the Write Enable Input | PASS
2 | Clearing the data | reset | HIGH | Reset, when high clears every bit of memory block and makes it 0. | PASS
 | Storing the data |  | LOW | Reset, when low allows the memory to store data as per its operation | PASS
3 | Stopping the data to be written to memory | Wr_en | LOW | Input lines should not be able to write any data into memory | PASS
 | Allowing the data to be written to memory |  | HIGH | Input lines should be able to write the data into memory | PASS
4 | Stopping the data to be read from memory | r_en | LOW | Output lines should not be able to read any data from memory | PASS
 | Allowing the data to be read from memory |  | HIGH | Output lines should be able to read data from memory | PASS
5 | When key/message input is less than 64 bits wide | Msg, key_in | <64bits | Input Data lines should be saved as it is and don’t care(x) will fill the rest in those empty slots | FAIL
6 | When key/message input is more than 64 bits wide | Msg, key_in | >64bits | Input Data lines will be taken till 64 bits and rest of the bits are truncated. | FAIL

## Slide 11: Results
Results of Verification using System Verilog

## Slide 12
  Encryption Block Result and Waveform

## Slide 13
  Decryption Block Result and Waveform

## Slide 14
  Memory Block Result and Coverage Analysis

## Slide 15
Coverage report of Memory Block

## Slide 16: Results
Results of Verification using UVM

## Slide 17
  Encryption Block Result and Coverage Analysis

## Slide 18
Coverage report of Encryption Block

## Slide 19
  Decryption Block Result and Coverage Analysis

## Slide 20
Coverage report of Decryption Block

## Slide 21
  Memory Block of Result and Coverage Analysis

## Slide 22
Coverage report of Memory Block

## Slide 23: References
http://page.math.tu-berlin.de/~kant/teaching/hess/krypto-ws2006/des.htm
https://verificationguide.com/systemverilog-examples/
http://www.testbench.in/TS_24_VERIFICATION_PLAN.html
https://www.design-reuse.com/articles/16141/verification-planning-for-core-based-designs.html
https://www.chipverify.com/systemverilog/systemverilog-tutorial

## Slide 24: Thank You.